## Slide 1
Year 8 Wall hanging Project : MAKING
PROJECT OBJECTIVES::
Design a product suitable for a specific person and need
Develop greater accuracy and apply components
Produce a 3D end product
CHECK your stitch settings
Length
Width
Straight stitch = L2 W0
Zig Zag stitch = L1.5 W5
SKILLS
Creating a template
Applying a seam allowance
Cutting fabric using a template
Pinning and tacking
Applique
Sewing on buttons
Basic sewing machine skills
Sewing on a zip
Making a pocket
Creating 3D parts
Correctly applying the ‘right side’ of the fabric
Applique
Cut out your template .
Pin your template to your fabric.
Cut around the template.
Pin and tack the shape onto your background fabric.
Sew around the edge of the shape.
Add further decoration if you want to.
Machine Applique
Sewing on a button…
Stitch Selector
Sewing binding…
Level 4
Use the correct tools and pay attention to accuracy
Level 5
Use a range of tools and components with precision
Level 6
Produce a successful end product and explain any changes you made
Hand Embroidery…
Cross Stitch
Right side – Template- Sew-
Seam allowance – Applique –
Embroidery- Fabric-Cotton
Seam allowance = 1.5cm
SAFETY: One person on a sewing machine / 4 H rules/ Carry equipment correctly
Blanket stitch
Double hem fold 1cm twice